## Slide 1
UNIT – III
ANALOG MULTIPLERS

## Slide 2
Analog Multipliers
Logarithmic Summing Technique (One Quadrant Device)
Pulse Height/Width Modulation Technique (One Quadrant Device)
Emitter Coupled Transistor Pair (Two Quadrant Device)
Gilbert Cell (Four Quadrant Device)
Variable Trans-conductance Technique
Types:
Symbol:

## Slide 3
Analog Multipliers
Introduction:
A multiple produces an output V0 which is proportional to the product of two inputs Vx and Vy. V0 = KVxVy where K is the scaling factor = (1/10) V-1.
An actual multiplier has its output voltage V0 defined by,
where φx and φy are the offsets associated with signals Vx and Vy, ε is the error signal associated with K and φ0 is the offset voltage of the multiplier output.

## Slide 4
Analog Multipliers
Terminologies associated voltage of the multiplier characteristics:
Accuracy:
This specifies the derivation of the actual output from the ideal output, for any combination of X and Y inputs falling within the permissible operating range of the multiplier.
Linearity:
This defines the accuracy of the multiplier. The Linearity Error can be defined as the maximum absolute derivation of the error surface. This linearity error imposes a lower limit on the multiplier accuracy.
The figure shows the response of the output as a function of one input voltage Vx when the other Vy is assumed constant.
It represents the maximum percentage derivation from the ideal straight line output.
An error surface is formed by plotting the output for different combinations of X and Y inputs.

## Slide 5
Analog Multipliers
Terminologies associated voltage of the multiplier characteristics:
Square law accuracy:
The Square – law curve is obtained with the X and Y inputs connected together and applied with the same input signal. The maximum derivation of the output voltage from an ideal square –law curve expresses the squaring mode accuracy.
Bandwidth:
The Bandwidth indicates the operating capability of an analog multiplier at higher frequency values. Small signal 3 dB bandwidth defines the frequency f0 at which the output reduces by 3dB from its low frequency value for a constant input voltage. This is identified individually for the X and Y input channels normally.
Bandwidth:
The quadrant defines the applicability of the circuit for bipolar signals at its inputs. First – quadrant device accepts only positive input signals, the two quadrant device accepts one bipolar signal and one unipolar signal and the four quadrant device accepts two bipolar signals.

## Slide 6
Analog Multipliers
Logarithmic summing Technique:
This technique uses the relationship
ln Vx + lnVy =ln(VxVy)
As shown in figure the input voltages Vx and Vy are converted to their logarithmic equivalent, which are then added together by a summer.
An antilogarithmic converter produces the output voltage of the summer. The output is given by,
Vz = ln-1(ln(Vx Vy )) = Vx Vy .
The relationship between I0 and VBE of the transistor is given by IC = I0e(VBE /VT ) .It is found that the transistor follows the relationship very accurately in the range of 10nA to 100mA. Logarithmic multiplier has low accuracy and high temperature instability.
This method is applicable only to positive values of Vx and Vy.
Limitation: This type of multiplier is restricted to one quadrant operation only.

## Slide 7
Analog Multipliers
Pulse Height/ Width Modulation Technique:
In this method, the pulse width of a pulse train is made proportional to one input voltage and the pulse amplitude is made proportional to the second input voltage.
Therefore,
Vx =Kx A, Vy =Ky t, and Vz =KzT where Kx, Ky, Kz are scaling factors. In figure A is the amplitude of the pulse, t is the pulse width and T is the area of the pulse. Therefore,
The modulated pulse train is passed through an integrated circuit.
Therefore, the output of the integrator is proportional to the area of pulse, which in turn is proportional to the product of two input voltages.

## Slide 8
Analog Multipliers
Emitter coupled Transistor pair:
The output currents IC1 and IC2 are related to the differential input voltage V1 by
where VT is thermal voltage and the base currents have been neglected.

## Slide 9
Combining above eqn., difference between the two output currents as,
Analog Multipliers
Emitter coupled Transistor pair:
The emitter coupled pair can be used as a simple multiplier using this configuration. When the differential input voltage V1 << VT, we can appropriate as given by,
∆IC =IEE ( V1/2VT)
The current IEE is the bias current for the emitter – coupled pair. If the current IEE is made proportional to a second input signal V2, then
IEE =K0 (V2 – VBE(ON))
Substituting above eqn. , we get
∆IC = K0V1 (V2 – VBE(ON))/2VT

## Slide 10
Analog Multipliers
Emitter coupled Transistor pair:
It is a simple modulator circuit constructed using a differential amplifier.
It can be used as a multiplier, provided V1 is small and much less than 50mV and V2 is greater than VBE (on).
But, the multiplier circuit shown in figure has several limitations.
The first limitation is that V2 is offset by VBE (on).
The second is that V2 must always be positive which results in only a two-quadrant multiplier operation.
The third limitation is that, the tanh (X) is approximately as X, where X = V1/2VT. The first two limitations are overcome in the Gilbert cell.

## Slide 11
Analog Multipliers
Gilbert Multiplier cell:

## Slide 12
The Gilbert multiplier cell is a modification of the emitter coupled cell and this allows four – quadrant multiplication. Therefore, it forms the basis of most of the integrated circuit balanced Multipliers.
Two cross- coupled emitter- coupled pairs in series connection with an emitter coupled pair form the structure of the Gilbert multiplier cell.
Analog Multipliers
Gilbert Multiplier cell:
The collector current of Q3 and Q4 are given by
Similarly, the collector current of Q5 and Q6 are given by

## Slide 13
Analog Multipliers
Gilbert Multiplier cell:
Collector current IC1 and IC2 of transistors Q1 and Q2 can be expressed as
Substituting the above equation in IC3 and IC4, we get
Similarly substituting Ic2 in Ic5 and IC6 , we get,

## Slide 14
Analog Multipliers
Gilbert Multiplier cell:
The differential output current I is given by
∆I =IL1 - IL2
= (IC3 +IC5) - ( IC4+IC6)
= (IC3 - IC6)-(IC4 - IC5)
∆I = IEE tanh( V1/2VT) tanh(V2/2VT)

## Slide 15
Analog Multipliers
Gilbert Multiplier cell:

## Slide 16
Analog Multipliers
Gilbert Multiplier cell :- Pre-Distortion Circuit:

## Slide 17
Analog Multipliers
Gilbert Multiplier cell :- Pre-Distortion Circuit:

## Slide 18
Analog Multipliers
Gilbert Multiplier cell :- Pre-Distortion Circuit:

## Slide 20
Analog Multipliers
Variable Transconductance Technique:

## Slide 21
The variable transconductance technique makes use of the dependence characteristic of the transistor transconductance parameter on the emitter current bias applied. A simple differential circuit arrangement depicting the principle is shown in figure.
The relationship between V0 and Vx . is given by V0 = gm RL VX where gm = IEE /VT is the transconductance of the stage.
Application of a second input Vy to the reference current source of the differential amplifier can vary gm.
Thus, if RE IEE >>VBE, the bias voltage Vy is related to IEE by the relation Vy = IEE RE.
Analog Multipliers
Variable Transconductance Technique:

## Slide 22
Analog Multipliers
Variable Transconductance Technique:
Then, the overall voltage transfer expression is given by
V0 = gm RLVx = (Vy/VTRE)VxRL
= VxVy RL/ VTRE

## Slide 23
Analog Multipliers
Analog Multiplier ICs:
Analog multiplier is a circuit whose output voltage at any instant is proportional to the product of instantaneous value of two individual input voltages.
Important applications of these multipliers are multiplication, division, squaring and square – rooting of signals, modulation and demodulation.
AD633

## Slide 24
Analog Multipliers
Analog Multiplier ICs:
The AD633 multiplier is a four – quadrant analog multiplier.
It possesses high input impedance; this characteristic makes the loading effect on the signal source negligible.
It can operate with supply voltages ranging from ±18V.
IC does not require external components.
The typical range of the two input signals is ±10V.
The schematic representation of an analog multiplier is shown in figure. The output V0 is the product of the two inputs Vx and Vy is divided by a reference voltage Vref.
Normally, the reference voltage Vref is internally set to 10V. Therefore, V0 =VxVy/10.
In other words, the basic input – output relationship can be defined by KVx Vy when K = 1/10, a constant. Thus for peak input voltages of 10V, the peak magnitude of output voltage is 1/10 *10 *10 =10V.
Thus, it can be noted that, as long as Vx < 10V and Vy < 10V, the multiplier output will not saturate.

## Slide 25
Analog Multipliers
Multiplier Quadrants:
Both the inputs can be positive or negative to obtain the corresponding output as shown in the transfer characteristics.
Applications of Multiplier ICs:
The multiplier ICs are used for the following purposes:
  Voltage Squarer
  Frequency doublers
  Voltage divider
  Square rooter
  Phase angle detector
  Rectifier

## Slide 26
Analog Multipliers
Voltage Squarer:
Figure shows the multiplier IC connected as a squaring circuit. The inputs can be positive or negative, represented by any corresponding voltage level between 0 and 10V.
The input voltage Vi to be squared is simply connected to both the input terminals, and hence we have, Vx = Vy = Vi and the output is V0 = KVi2.
The circuit thus performs the squaring operation. This application can be extended for frequency doubling applications.

## Slide 27
Analog Multipliers
Frequency doublers:

## Slide 28
Analog Multipliers
Frequency doublers:
Figure shows the squaring circuit connected for frequency doubling operation. A sine-wave signal Vi has a peak amplitude of Av and frequency of f Hz. Then, the output voltage of the doublers circuit is given by
Assuming a peak amplitude Av of 5V and frequency f of 10KHz, V0 =1.25–1.25 cos2 20000) t. The first term represents the dc term of 1.25V peak amplitude.
The input and output waveforms are shown in figure. The output waveforms ripple with twice the input frequency in the rectified output of the input signal. This forms the principle of application of analog multiplier as rectifier of ac signals.
The dc component of output V0 can be removed by connecting a 1µF coupling capacitor between the output terminal and a load resistor, across which the output can be observed.

## Slide 29
Analog Multipliers
Voltage Divider:
In voltage divider circuit the division is achieved by connecting the multiplier in the feedback loop of an op-amp.
The voltages Vden and Vnum represent the two input voltages, Vdm forms one input of the multiplier, and output of op-amp VoA forms the second input.
The output VOA forms the second input. The output VOM of the multiplier is connected back of op- amp in the feedback loop. Then the characteristic operation of the multiplier gives
Vom = KVOA Vdm (1)

## Slide 30
As shown in figure, no input signal current can flow into the inverting input terminal of op-amp, which is at virtual ground. Therefore, at the junction a, i1 + i2 =0, the current i1 = Vnum / R, where R is the input resistance and the current i2 = Vom /R. With virtual ground existing at a,
  i1+i2 = Vnum / R + Vom /R = 0
    KVOA Vden = - Vnum
or
  voA=- vnum/Kvden
where Vnum and Vden are the numerator and denominator voltages respectively.
Therefore, the voltage division operation is achieved. Vnum can be a positive or negative voltage and Vden can have only positive values to ensure negative feedback.
When Vdm is changed, the gain 10/Vdm changes, and this feature is used in automatic gain control (AGC) circuits.
Analog Multipliers
Voltage Divider:

## Slide 31
Analog Multipliers
Square Rooter:
The divider voltage can be used to find the square root of a signal by connecting both inputs of the multiplier to the output of the op-amp. Substituting equal in magnitude but opposite in polarity (with respect to ground) to Vi. But we know that Vom is one- term (Scale factor) of V0 * V0 or -Vi = Vom = V2/10
Solving for V0 and eliminating √-1 yields. V0 = √10|Vi |
Eqn. states that V0 equals the square root of 10 times the absolute magnitude of Vi.
The input voltage Vi must be negative, or else, the op-amp saturates.
The range of Vi is between -1 and -10V. Voltages less than -1V will cause inaccuracies in the result.
The diode prevents negative saturation for positive polarity Vi signals. For positive values of Vi the diode connections are reversed.

## Slide 32
Analog Multipliers
Phase Angle detector:

## Slide 33
The multiplier configured for phase angle detection measurement is shown in figure. When two sine-waves of the same frequency are applied to the inputs of the multiplier, the output V0 has a dc component and an AC component.
The trigonometric identity shows that
Sin A sin B =1/2 (cos (A-B) – cos (A+B)).
When the two frequencies are equal, but with different phase angles, e.g. A=2πft +θ for signal Vx and B= 2πft for signal Vy, then using the identity
[sin (2πft+θ)][sin2πft)]=1/2[cosθ-cos(4πft+θ)]=1/2(dc- the double frequency term)
Analog Multipliers
Phase Angle detector:

## Slide 34
Analog Multipliers
Phase Angle detector:
Therefore, when the two input signals Vx and Vy are applied to the multiplier, V0 (dc) is given by
where Vxp and Vyp are the peak voltage amplitudes of the signals Vx and Vy. Thus, the output V0(dc) depends on the factor cos θ. A dc voltmeter can be calibrated as a phase angle meter when the product of Vxp and Vyp is made equal to 20. Then, a (0-1) V range dc voltmeter can directly read cos θ, with the meter calibrated directly in degrees from a cosine table. The input and output waveforms are shown in figure.
Then the above eqn becomes V0 (dc) = cos θ, if we make the product Vxp Vyp = 20 or in other words, Vxp – Vyp = 4.47V.

## Slide 35
http://www.brainkart.com/article/Analog-Multipliers_36018/
https://www.youtube.com/watch?v=Bdng-6N00G8
GILBERT MULTIPLIER CELL | ANALOG MULTIPLIER USING EMITTER COUPLED TRANSISTOR PAIRS